## Slide 1
static control made Easy!
Introducing a new level of static control; The heart of the new IQ Easy platform is the Manager IQ Easy. It comprises of a Control unit with a 7” LCD touch screen, provides information from all the connected devices and makes it easy to change and monitor status and parameters. Up to 6 IQ devices can be directlyconnected to the Manager IQ Easy. The 24V DC power distribution is routed via the Manager, so no extra cables! This makes the connection of a device even easier than connection to a single desktop power supply.
The Manager IQ is available in 2 versions:
g Input voltage 100 – 240V /50-60 Hz
This unit converts the input voltage to 24V DC and provides power to all 6 connected devices.
g Input voltage 24V DC
This model needs a 24V power input provided by the user.
Further extension of devices is possible using the Extension IQ Easy. This adds another 6 devices to the system with a maximum of 30.
2 ports on each Manager or Extension are available for the connection of previous (non IQ) Easy products e.g. Performax Easy.
Interfacing
Communication to machine interfaces is provided.
Analogue and digital inputs,outputs and several serial ﬁeldbus protocols can be used. Also Ethernet and USB ports are available for many functions.
Pro-Active ionisation control
Through Simco-Ion’s patented technology of upstream charge evaluation, it is possible to ﬁne tune neutralisation of static in combination with a Performax IQ Easy anti-static bar. Adding a Sensor IQ Easy to the system will allow the user to measure the downstream charge on the material. The system can also be perfected further to enhance eﬃciency and allow quality control. Closed loop measuring and adjustment of the static bar output will guarantee an extremely low level of residual charge.
Data logging
Al device and process parameters are logged in real time and can be made visible on the LCD screen or downloaded through the Ethernet interface.
Features
g 7” full colour touch screen. g Information is colour coded. g Controls up to 30 devices. g Connection up to 6 devices.
g Analogue & digital inputs and outputs.
g Serial ﬁeldbus interfaces.
g Ethernet interface.
g USB interface.
Product Specifications
Static elimination Power Units
Manager IQ Easy
2 | www.simco-ion.co.uk/our-products/static-elimination/power-units/manager-iq-easy | Static elimination | Power Units | Manager IQ Easy

## Slide 2
300
233
150
300
233
150
Static elimination | Power Units | Manager IQ Easy
Easy cable access
Panel mounting
Connection of up to 6 devices
7” full colour touch screen
Technical drawing Manager IQ Easy
Easy mounting
2 | www.simco-ion.co.uk/our-products/static-elimination/power-units/manager-iq-easy | Static elimination | Power Units | Manager IQ Easy

## Slide 3
Additional safety connector
Optional
g Manager IQ Easy with additional safety circuit.
The Manager IQ Easy can be supplied with an additional safety circuit that will cut the 24V power to all connected devices. The circuit is controlled by double contacts and double feedback signal according to the machine safety directive.
Static elimination | Power Units | Manager IQ Easy
2 | www.simco-ion.co.uk/our-products/static-elimination/power-units/manager-iq-easy | Static elimination | Power Units | Manager IQ Easy

## Slide 4
Simco-Ion Netherlands
Postbus 71
Lochem, The Netherlands NL-7240 AB
Tel: +31 (0)573 288333
Fax: +31 (0)573 288380
general@simco-ion.nl www.simco-ion.nl
Static elimination | Power Units | Manager IQ Easy
4 | www.simco-ion.co.uk/our-products/static-elimination/power-units/manager-iq-easy | Static elimination | Power Units | Manager IQ Easy